## Slide 1
Under the Guidance of Dr. Prakash Pawar
Annamaneni Rohit - 20BCS019
Sai Tarun Parasa - 20BCS096
Venkata Sai Nikhil Vemprala - 20BCS135
Sowmya S - 20BDS053
OPTIMIZATION AND SCHEDULING APPLIANCES PRIORITY FOR
Residential Buildings

## Slide 2
CONTENT
03
01
02
Introduction
Related work
Problem
formulation
04
Objective function
& Constraints
05
Algorithms
06
Results
07
Conclusion

## Slide 3
INTRODUCTION
  Smart Grids (SGs) introduced to address energy challenges.
  Bi-directional SGs enable efficient information exchange between providers and consumers.
  Demand Side Management (DSM) strategies play a pivotal role.
  DSM optimizes energy consumption by shifting usage from peak to off-peak hours.
  Key DSM components:
    Demand Response (DR)
    Load Management.
  These elements lead to a more efficient and cost-effective electricity distribution system.

## Slide 4
M. A. A. Pedrasa, T. D. Spooner and I. F. MacGill, "Scheduling of Demand Side Resources Using Binary Particle Swarm Optimization,"
RELATED WORK
PAPER 1
  Minimize the total cost.
  Parameter Tuning
  Comparision between FDP and BPSO
  Subworms are used for increasing the solution probabilities
PAPER 2
PAPER 3
  Minimizing PAR and electricity cost.
  EWA for generatig new solutions
  HSA selects new solution from memory.
  Hybrid EHSA (EWA + HSA)
  Real Time Pricing (RTP)
  Time of Use (TOU)
  Critical Peak Pricing (CPP)
  Optimzing using TLBO and SFL
  Shiftable, Sheddable and Non-Sheddable load categories
Derakhshan, Ghasem & Shayanfar, Heidarali & Kazemi, Ahad. (2016). The optimization of demand response programs in smart grids.
Hassan, Smart Grid Energy Optimization and Scheduling Appliances Priority for Residential Buildings through Meta-Heuristic Hybrid Approaches.

## Slide 5
PROBLEM FORMULATION
  The problem at hand requires a solution which is a curtailment schedule.
  Solution is a (t,n) shaped matrix where t = number of hours and n = number of appliances.
  solution(t, i) is equal to 1 if the i th appliance is being curtailed during the hour t.
  Each of the appliances is given a capacity and a curtailment rate which is indicative of the cost incurred from curtailing the appliance.
  The appliances also have an associated maximum off duration and minimum on duration that they must adhere to.

## Slide 6
Additionally, the appliances are divided into three priority levels. Each of the priority levels indicates how frequently the appliances can be curtailed with priorities ranging from 1 to 3.
PROBLEM FORMULATION

## Slide 7
OBJECTIVES
  Minimize curtailment cost to check hourly curtailed load.
  Minimize instances of under curtailment.
  Prevent repeated curtailment of appliances.
  Adhere to min on hours and max off hours.
  Minimize peak to average ratio to reduce excess curtailment.

## Slide 8
OBJECTIVE FUNCTION
CURTAILMENT COST
UNDER CURTAILMENT

## Slide 9
CURTAILMENT FREQUENCY
OFF AND ON PENALTY
OBJECTIVE FUNCTION

## Slide 10
PAR RATIO
Based on empirical results, it was found that the following weights provide the best representation of solution fitness
OBJECTIVE FUNCTION

## Slide 11
ALGORITHMS
Binary particle swarm optimization

## Slide 12
ALGORITHMS
Differential evolution

## Slide 13
ALGORITHMS
Harmonic Search Algorithm

## Slide 14
RESULTS

## Slide 15
RESULTS

## Slide 16
RESULTS

## Slide 17
Algorithm | Priority 1 | Priority 2 | Priority 3
BPSO | 3 | 11 | 10
Differential evolution | 4 | 10 | 8
Harmonic search | 54 | 42 | 39
RESULTS
Priority wise curtailment freq

## Slide 18
Algorithm | PAR
BPSO | 1.090
Differential evolution | 1.102
Harmonic search | 1.342
RESULTS
Algorithm | Average iteration runtime
BPSO | 0.401 secs
Differential evolution | 0.099 secs
Harmonic search | 0.015 secs
Peak to average ratios
Algorithm runtimes
Algorithm | Fitness
BPSO | 152366.0
Differential evolution | 201868.0
Harmonic search | 9456108.8
Fitness comparision

## Slide 19
BPSO provided valuable insights into the efficient management of energy consumption within residential buildings.
BPSO effectively minimized peak loads while maintaining optimal appliance schedules.
Additionally, BPSO Algorithm has proven to be highly efficient in terms of Peak to average ratios when compared to Differential Evolution and Harmonic Search.
CONCLUSION

## Slide 20
M. A. A. Pedrasa, T. D. Spooner and I. F. MacGill, "Scheduling of Demand Side Resources Using Binary Particle Swarm Optimization," in IEEE Transactions on Power Systems, vol. 24, no. 3, pp. 1173-1181, Aug. 2009, doi: 10.1109/TPWRS.2009.2021219.
REFERENCES
REFERENCES 1
REFERENCES 2
REFERENCES 3
Derakhshan, Ghasem & Shayanfar, Heidarali & Kazemi, Ahad. (2016). The optimization of demand response programs in smart grids. Energy Policy. 94. 295-306. 10.1016/j.enpol.2016.04.009.
Hassan, C.A.u.; Iqbal, J.; Ayub, N.; Hussain, S.; Alroobaea, R.; Ullah, S.S. Smart Grid Energy Optimization and Scheduling Appliances Priority for Residential Buildings through Meta-Heuristic Hybrid Approaches. Energies 2022, 15, 1752.

## Slide 21
THANK YOU